## Slide 1
Do we actually need both Speculative and non-speculative counter ?
We don’t need Speculative counter, only non-speculative is enough for counting loop trip count

## Slide 2: Where speculative iteration counter is used?
Speculative iteration counter is used to override the branch predictor's misprediction
Check for PC in LTB
If PC found in LTB
PC Not found in LTB
TC == SIC
Check Confidence bit
Predict branch not taken
(loop exit)
SIC ++
Branch Predictor make decision
Yes
Yes
No
Yes
No
No
If they match and the predictor is confident, it safely overrides the baseline branch predictor by forcing a "Not-Taken" prediction to correctly terminate the loop
TC == SIC
Check Confidence bit
Predict branch not taken
(loop exit)
Phase 1: Branch Prediction

## Slide 3
PC | TC | SC | NSC | Conf
New loop termination buffer
PC | TBA | TC | NSC | Pf_C
TC: Trip counter
SC: Speculative Iteration counter
NSC : Non-Speculative iteration counter
Conf : Confidence bit
TBA : Target Branch address
Pf_C : Count prefetch issued for a PC

## Slide 4
Test Cases

## Slide 5: Loop iteration count with Nested loop
Testcase 2

## Slide 6: Loop iteration count, loop with if break condition without
Testcase 3

## Slide 7: Loop iteration count, loop with if condition
Testcase 4

## Slide 8: How do we capture this behavior ?
Testcase 4
The iteration count of loop is affected because of "IF condition" with break statement
To capture this behavior, we need to find in which loop does this "IF condition" present because we could have multiple loops in our program
There are two trends of "IF condition" statement first when it terminate a loop and when it does not terminate a loop

## Slide 9: How do we capture this behavior ?
Testcase 4
When loop get terminated
PC: Loop Start
PC: Loop End
PC: IF Cond. Check
PC: IF cond. target
Taken only when IF condition is satisfied
We will search above pattern in loop buffer and then update the trip count of loop

## Slide 10: How do we capture this behavior ?
Testcase 5
2. When loop does not get terminated
PC: Loop Start
PC: Loop End
PC: IF Cond. Check
PC: IF cond. target
We will search above pattern in loop buffer

## Slide 11: How do we know which branch path is taken for trip count ?
To learn about the path taken by branch we need to make some changes in our loop buffer
PC | TBA | TC | NSC | IEB | ITA | Pf_C
PC : Program Counter
TBA : Target branch address
TC : Trip count
NSC: Non-speculative iteration counter
IEB : IF-Else Branch address
ITA : IF-Else traget address
Pf_C: Prefetch counter

## Slide 12: How do we know which branch path is taken for trip count ?
PC | TBA | TC | NSC | IEB | ITA | Pf_C
40046e | 400451 | 300000 | 270919 | 400465 | 400472 | 0

## Slide 13: Testcase 6
PC | TBA | TC | NSC | IEB | ITA | Pf_C
40048c | 400451 | 699999 | 440633 | 400465 | 400488 | 0
400484 | 400470 | 2001 | 0 | 0 | 0 | 0

## Slide 14: Testcase 7

## Slide 15: What is the accuracy of predicted loop iteration count ?

## Slide 16: Simulation parameter
Processor | Intel alder lake
Core | Out-of-order, bimodal branch predictor, 4 GHz with 6-issue width, 4-retire width, 352-entry ROB
TLBs | L1 iTLB/dTLB: 64 entries, 4-way, 1 cycle STLB: 1536 entries, 12-way, 8 cycles
L1I | 64 KB, 8-way, 4 cycles, 8 MSHRs, LRU
L1D | 48 KB, 12-way, 5 cycles, 16 MSHRs, LRU
L2 | 2 MB, 16-way, 15 cycles, 32 MSHRs
LLC | 3 MB, 16-way, 35 cycles, 64 MSHRs
Cache hierarchy | Non-inclusive
DRAM | Controller: One channel/4-cores, 6400 MTPS, write watermark: 7/8th, Chip: 4 KB row-buffer, open page, tRP: 12.5 ns, tRCD: 12.5 ns, tCAS: 12.5 ns
Notes: Processor used is intel alder lake with L1d __ , L2 512kb , LLC 2mb

## Slide 17: Loop iteration count accuracy for SPEC CPU2017 workload
We achieve 90% or more accuracy for half of the traces but the overall accuracy across workload is ~84%
Data prefetcher
L1D: Berti, L2: IP Stride
Replacement policy
L2: SRRIP, LLC: Mockingjay

## Slide 18: What are we missing?
R
A
B
D
E
G
C
F
H
I
J
R
A
B
D
E
G
C
F
H
I
J
RADCHJ : 20
R
A
B
D
E
G
C
F
H
I
J
RADCI : 40
RAEF : 10
RBG : 20
Loop PC

## Slide 19: New design of loop iteration count buffer
Program Counter | Target Address | Iteration Count | Non-Speculative Counter | Prefetch Counter
Branch History | Iteration count

## Slide 20: Loop iteration count accuracy for SPEC workload
We achieve ~99% accuracy in SPEC CPU17 workload
Data prefetcher
L1D: Berti, L2: IP Stride
Replacement policy
L2: SRRIP, LLC: Mockingjay

## Slide 21: Thank You